GNSS/GPS Receiver Checklist
- Before you leave staging:
  - Check Batteries
    - Check that the batteries in the GPS have adequate charge.
    - Check that you have spare batteries for the GPS.
  - Find out the Datum and Coordinate system in use for this incident.
    - Standard values are:
      - Map Datum: WGS84
      - Position Format: US National Grid (USNG)
  - Set your GPS to the appropriate Datum and Coordinate System.
  - Set your GPS to report bearings relative to True North or Magnetic North as appropriate.
- When you arrive at a dropoff/pickup point for your assignment:
  - Make sure your GPS has an accurate position.
    - Lock on 4 or more satellites.
    - 3D positioning.
    - Horizontal position accurate to within about 15 meters or better.
  - Save the current location as a waypoint. Name the Waypoint (e.g. Team 4 drop off)
  - Write down the coordinate of the current location.
  - Save the current track.
  - Clear the current track.
  - Calibrate the GPS compass.
  - Confirm that your GPS is recording the track.
- When you begin your assignment:
  - Save the current location as a waypoint.
- When you locate something during your assignment:
  - Save the current location as a waypoint.
  - Write down the location and the name/number of the waypoint.
- When you complete your assignment:
  - Save the current track with a clear name.

US National Grid: Describing a 10 meter square

Communicating position locally: 99250895
(Easting is 9925, Northing is 0895. Read as: 99250895)
Communicating position Regionally: BH 99250895
Communicating position Globally: 19T BH 99250895

Entering into GPS: You need the full coordinate: 19T BH 9925008950
Enter to 1 meter resolution (5 digit easting and 5 digit northing).
(Add in zero for 1 meter resolution in Easting, and zero for 1 meter resolution in Northing).